## Slide 1
Abstract
This project aims to harvest and integrate existing data about subsurface data related to existing construction, utility failures, and storm information (both historical and predicted) and to use this information as the basis for future, neighborhood-level, performance, as well as infrastructure investment planning. This is done in a Geographic Information System for a 1km2 area in the Sunset Park neighborhood of Brooklyn. The immediate goal is to show the horizontal and vertical relationship between underground structures. Self-reporting from 311 calls [2010-present] were then overlaid, along with FEMA flooding predictions. A machine learning approach is used to predict foundation information and flooding.
Project Background
New York City has a long, rich history filled with aging infrastructure and previous generations of construction. While the information for and problems of aboveground constructions are common and relatively well understood, collecting and integrating subsurface elements and the in-situ natural materials pose major challenges due to the complexity, incompleteness, and inconsistency of the available data. These are in addition to technical difficulties in processing, storing, and integrating the data and uncertainties as to what historical information is still relevant. Having such information can be a critical advantage in a wide range of planning, construction, and disaster mitigation efforts.
Conclusions & Future Plan
The overall data collection and cleaning process is shown in Fig. 1. This involved harvesting information from historic fire insurance maps and open access information from State, City and national GIS layers. Building machine learning models from Sklearn were applied. For inferring building foundation, R2 = 0.7614 (Fig. 3). For future complaints prediction, R2 = 0.5631(Fig. 4).To increase reliability, future work will focus on introducing geological and hydrological data.
Methods
Figure 2: ArcGIS Map of Sunset Park
Works Cited
[1] “PLUTO and MapPLUTO.” Nyc.Gov, www1.nyc.gov/site/planning/data-maps/open-data/dwn-pluto-mappluto.page. Accessed 2 Aug. 2020.
‌[2] “Google Map View of 311 Reports.” NYC Open Data, https://data.cityofnewyork.us/Social-Services/Google-map-view-of-311-reports/dtiu-hq3j
[3] “Building Footprints.” NYC Open Data, https://data.cityofnewyork.us/Housing-Development/Building-Footprints/nqwf-w8eh
[4] “Brooklyn Historical Map”, Greatest Grid, https://thegreatestgrid.mcny.org
Acknowledgements
The authors thank NYU Tandon School of Engineering’s Office of Undergraduate Academics for generous funding of the project.
Above and below ground construction data of Sunset park area is collected through NYC Open data and NYC Department of Planning and converged by. A machine learning model for estimating foundation is constructed to enrich the datasets. 311 complaints data is analyzed by Python and predicted by machine learning models.
Collect above- below ground construction data
Layer ArcGIS map with collected data
Analyze and estimate under- ground structures
Overlay pipes, subways, & other infrastructures
Combine historical maps and current data
Predict building foundations
Analyze 311 complaints data
75%- training
25%- confirming
Estimate with trained model
Extract water problems
(2010-2019)
ID catch basin clogged, sewer backup, & flooding
*Machine learning involved
Known Data
Unknown Data
Create 3D map as reference for city planning
Predict future complaint occurrence
75%- training
25%- confirming
ArcGIS
(Fig. 2)
Figure 4: Plumbing Complaint Predict
Figure 3: Foundation Depth Predict
Figure 1: Methodology
Results
For result, the subsurface map of Sunset park area is constructed on ArcGIS which includes layers of wires, pipes, subways, and other underground urban structures. Based on the machine learning model, the accuracy of predicting future plumbing complaints is 56.31%.
Subsurface Testbed
New York University Tandon School of Engineering
Supervisor, New York University Tandon School of Engineering
Professor, Center for Urban Science and Progress
Xinru Li,1 Silvia Wei,1 Michael Stanley,2 Debra F. Laefer, PhD3
Contact: corresponding author’s email
University Logo